## Slide 1: Building the Backbone: How Foundational Processes and EAM Solutions Transform Facilities Management
Bryan Decker
CEO
Steadfast Operations

## Slide 2: Outline
Setting up A Solid Foundation
SECTION 1
Hexagon EAM: Turning Execution Into Control
SECTION 2
Governance + Operating Rhythm
SECTION 3
A Practical Roadmap
SECTION 4
The Backbone Promise
SECTION 5

## Slide 3: Setting Up A Solid Foundation

## Slide 4: Why This Matters
Every outage has a story: a missed inspection, weak turnover, poor change control, incomplete closeout, wrong part, unclear ownership.
Leaders care about:
  availability / uptime risk
  safety and regulatory exposure
  customer/SLA impact
  audit readiness
  predictable OPEX and defensible CAPEX
Operators care about:
  fewer emergencies
  clearer priorities
  better planning windows
  faster restoration and fewer repeat events
“We don’t ‘manage work’—we manage risk through work.”
Add text or image

## Slide 5: The Backbone Model
Foundational programs define how work is done.
Hexagon EAM enforces standards and captures the evidence trail:
  assets → work → parts → inspections → costs → history
Outcome: risk-based decision-making and repeatable performance.
“No standards → no reliable data. No reliable data → no control.”
Add text or image

## Slide 6: Foundational Program 1: Operations Readiness
Operations Readiness: The “Day-1 Reliability” Program
Applies to:
  new builds, expansions, retrofit/refresh, major equipment replacements, vendor transitions
Readiness checklist categories:
  people (roles, coverage model, training/certification)
  process (SOP/MOP/EOP finalized; change control operational)
  tools (Hexagon EAM configured; mobile; reporting)
  spares/vendors (critical spares on hand; SLAs active; escalation contacts)
  data (assets loaded; PMs active; warranties; test reports; O&M manuals; as-builts)
“Readiness is where reliability is won—before the first real incident happens.”

## Slide 7: Foundational Program 2: Asset Management
Asset Management: What “Good” Looks Like
Complete and accurate asset hierarchy aligned to how you operate:
  campus → building → rooms/whitespace → systems → equipment → components
Criticality tied to consequence (not replacement cost):
  safety impact, redundancy impact, customer load impact, time-to-fail exposure
Configuration matters: what’s installed, where, and how it’s configured (feeds change control and readiness).
Lifecycle visibility for major risk assets:
  UPS modules, batteries, switchgear, breakers, generators, ATS/STS, chillers
“If we can’t trust the asset register, we can’t trust the operation.”
Add text or image

## Slide 8: Asset Management Deliverables (What You Build)
Golden asset register in Hexagon EAM (ownership + governance defined)
Minimum data standards for mission critical assets:
  location, manufacturer/model/serial, redundancy group, upstream/downstream dependencies, warranty, PM strategy
Critical asset lists by system and redundancy group (what truly threatens uptime)
Standard job plans / PM library for critical systems
Spare parts classification:
  critical spares (no-stockout tolerated), lead times, alternates, vendor agreements
“This is the foundation for controlling uptime risk and capital surprises.”
Add text or image

## Slide 9: Foundational Program 3: Work Management
Standard workflow:
  Initiation → Plan → Schedule → Prepare → Execute → Close → Learn
Mission critical additions:
  risk assessment for any work impacting redundancy
  MOP/SOP/EOP linkage (Method of Procedure / Standard Operating Procedure / Emergency Operating Procedure)
  permit-to-work / LOTO / access controls as applicable
  maintenance window management and stakeholder notification
“Work management is change risk management.”
Add text or image

## Slide 10: Planning & Scheduling: What Separates Good From Great
Plan quality drives execution quality:
  clear scope, prerequisites, parts, tools, permits, steps, backout plan
Schedule discipline:
  protect the weekly schedule; define what qualifies as true break-in work
Coordination across teams:
  facilities, controls, IT/network, security, vendors—because misalignment creates risk
Closeout discipline:
  accurate labor/materials, completion notes, test results, condition readings, cause codes
“If it’s not closed correctly, it didn’t happen—and it can’t protect us later.”
Add text or image

## Slide 11: Work Management KPIs That Matter
Planned vs unplanned work (% planned)
Schedule compliance (and reasons for misses)
Work order aging by priority and by criticality
PM compliance on critical assets (including deferrals and approvals)
Maintenance window adherence (started/ended on time; redundancy maintained)
Repeat corrective work on the same asset/system
MTTR for critical systems + restoration time trend
“These KPIs are early warning signals for downtime risk.”

## Slide 12: Foundational Program 4: Incident Management
Define tiers clearly:
  Alarm/Event (signal) vs Incident (service impact or elevated risk) vs Major Incident (customer/SLA/redundancy breach)
Standardize:
  severity levels, response targets, escalation paths, communications templates
Capture near misses:
  loss of redundancy, abnormal readings, nuisance trips—these are free lessons
“The best outage is the one you prevented because you treated a near miss seriously.”

## Slide 13: Incident Output: Closing the Loop Into Work
Every significant incident produces:
  immediate response record
  follow-up corrective work orders
  preventive actions (procedure update, training, inspection frequency changes, spares adjustments)
Right-size RCA:
  major incidents get structured RCA + tracked corrective actions
  routine issues get fast causal coding and trend monitoring
“Incident management isn’t reporting—it’s risk reduction”

## Slide 14: Hexagon EAM: Turning Execution into Control
Add text or image

## Slide 15: Hexagon EAM’s Role (What “System of Record” Means Here)
Hexagon EAM should be the authoritative record for:
  assets and hierarchy
  job plans / PMs / inspections
  work order history and costs
  failure and cause coding
  compliance evidence
  materials and critical spares
The objective: standardization, traceability, and decisions based on reality.
“Software doesn’t create discipline—but it can enforce it and make it visible.”

## Slide 16: Minimum Viable Data Model
Asset attributes that matter:
  redundancy group / system path
  upstream/downstream dependency notes
  criticality rating
  warranty + vendor/service contract linkage
Work order fields that matter:
  priority + risk category
  planned steps / MOP reference
  permits/LOTO indicators
  test/verification results
  downtime/redundancy impact flag
Failure data:
  standardized problem/cause/remedy codes for trend analysis
“Data quality is a leadership expectation, not a side project”

## Slide 17: Risk Reduction Use Cases (Powered by Hexagon EAM Data)
Critical PM deferral risk:
  show deferrals by redundancy group, required approvals, and cumulative exposure
Repeat failure elimination:
  identify chronic assets (same UPS/breaker/CRAH repeatedly) and drive permanent fixes
Compliance evidence on demand:
  inspection history, test results, certification records, calibration logs
Critical spares risk:
  stockouts, long lead times, consumption patterns tied to failure history
Vendor performance risk:
  response time, completion quality, rework rate, cost variance
“We reduce risk by making it measurable, owned, and acted on”

## Slide 18: Operational Excellence Use Cases (Availability + Efficiency)
Shift-left from reactive to planned work:
  increase planned %, decrease emergency changes
Reliability improvement targeting:
  focus on the small set of assets driving most incidents and near misses
Better maintenance windows:
  fewer overruns, better coordination, less customer anxiety
CAPEX justification:
  replacements based on risk + lifecycle cost + incident history, not age alone
Performance transparency:
  dashboards by site/system (electrical vs mechanical), by redundancy group, by vendor
“Excellence is repeatable outcomes—measured, managed, improved”

## Slide 19: Governance + Operating Rhythm (The Non-Negotiables)
Define owners for:
  asset master data
  PM library / job plans / procedures
  priority model and triage rules
  reporting and KPI review cadence
Operating rhythm:
  daily triage + event review
  weekly scheduling + readiness for windows
  monthly reliability review (bad actors, PM effectiveness, repeat incidents)
  quarterly risk/capex review (critical asset condition + exposure)
“If the standards aren’t owned, the operation will drift—and drift creates outages”

## Slide 20: A Practical Roadmap (How You Implement Without Disrupting Ops
Phase 1: Stabilize
  triage/priority definitions, backlog visibility, critical asset identification, closeout standards
Phase 2: Standardize
  asset hierarchy cleanup, PM/job plan standardization, planning/scheduling cadence, inspections structure
Phase 3: Optimize
  reliability initiatives (targeted RCA), spares optimization, risk dashboards, capital planning integration
“We build momentum with measurable wins—without betting uptime on a big-bang change”

## Slide 21: The Backbone Promise
Less risk: fewer loss-of-redundancy events, fewer major incidents, stronger audit posture
More reliability: higher planned work, better schedule compliance, fewer repeats
More control: defensible decisions on spares, vendors, and capital timing
Final message: Foundations first. Hexagon EAM as the enabler. Operational excellence as the outcome.
“When the backbone is strong, uptime stops being a slogan and becomes a managed result”

## Slide 22: Questions